## Slide 1
January 8, 2019
Benefit Cost Analysis (BCA) Overview
Cal OES

## Slide 2: Training Introduction
Welcome
Purpose of training
Instructor introductions
Survey of attendees – BCA experience and expectations for the training
Format of training sessions

## Slide 3: Agenda
BCA resources
General concept of a BCA
Determining benefits for a hazard mitigation project
Components of a BCA
Documenting the BCA
Using the FEMA BCA tool

## Slide 4: BCA Resources

## Slide 5: BCA Resources
Hazard Mitigation Assistance (HMA) Guidance and Addendum
BCA Reference Guide
Supplement to the BCA Reference Guide
HMA Job Aids
FEMA Building Science publications
FEMA BCA helpline (email and phone)
OES/Hagerty post-training consultation
Linked on Cal OES HMGP web page under “Benefit Cost Analysis Overview Cover Sheet”
Many other subject matter-specific resources

## Slide 6: General Concept of a BCA

## Slide 7: General Concept of a BCA
A BCA is the method by which the future benefits of a hazard mitigation project are determined and compared to its costs
The end result is a Benefit-Cost Ratio (BCR), which is calculated by a project’s total benefits divided by its total costs
A project is considered to be cost effective when the BCR is 1.0 or greater, indicating the benefits of a prospective hazard mitigation project are sufficient to justify the costs
The benefits are the net present value of the reduction in damages and losses over the useful lifetime of the project, using FEMA’s 7% discount rate
The present value calculation is done automatically in the BCA software

## Slide 8: General Concept of a BCA
FEMA requires a BCA to validate cost effectiveness of proposed hazard mitigation projects prior to funding. There are two drivers behind this requirement:
The Office of Management and Budget’s (OMB) Circular A-94 Revised, “Guidelines and Discount Rates for Benefit-Cost Analysis of Federal Programs”
  The goal of Circular A-94 is to promote efficient resource allocation through well-informed decision-making by the Federal Government
  FEMA’s BCA Toolkit has been developed to meet the guidelines published in Circular A-94
The Stafford Act
  The Stafford Act authorizes the President to establish a program to provide technical and financial assistance to state and local governments to assist in the implementation of hazard mitigation measures that are cost effective and designed to substantially reduce injuries, loss of life, hardship, or the risk of future damage and destruction of property

## Slide 9: General Concept of a BCA
Most of the focus of a BCA is on the benefits side
Costs are usually relatively easy, though they must come from a good source AND they must be more or less accurate, because they are used by States and FEMA in budgeting for the grant programs

## Slide 10: Calculating Benefit Cost Ratio (BCR)
Benefits
Costs
Benefit-Cost Ratio (BCR)

## Slide 11: General BCA Example
Your mechanic recommends replacing a part on your car to reduce problems in the future.
  The replacement part with labor will cost $2,500
  The mechanic estimates the old part will need service twice a year that will cost $300 each
  The mechanic estimates the new part will only need service once a year for a $150 service
  You only plan to use the car for 7 more years
Would you pay for the replacement part?

## Slide 12: General BCA Example
Your mechanic recommends replacing a part on your car to reduce problems in the future.
  The replacement part with labor will cost $2,500
  The mechanic estimates the old part will need service twice a year that will cost $300 each
  The mechanic estimates the new part will only need service once a year for a $150 service
  You only plan to use the car for 7 more years
Would you pay for the replacement part?
  Without replacement, expect to pay $600 per year in services
  With replacement, expect to pay $150 per year in services
  Savings in service costs is $450/year, or $450*7 = $3,150 over 7 years
  BCR = 1.26

## Slide 13: Example of a Hazard Mitigation Project
First Floor Elevation
(FFE) = 500’
Before Mitigation (Pre-Mitigation)

## Slide 14: Example of a Hazard Mitigation Project
5-year flood = 500’
(FFE = 500’)
100-year flood = 504’
10-year flood = 502’
Before Mitigation (Pre-Mitigation)

## Slide 15: Damages to Structure
Pre-Mitigation
Flood Depth (feet) | Annual Probability of Flooding | Scenario Damages and Losses | Expected Annual Damages and Losses
0 | 0.20 (5-year flood) | $6,400 | $1,280
2 | 0.10 (10-year flood) | $24,500 | $2,450
4 | 0.01 (100-year flood) | $32,100 | $321
Total Expected Annual Damages and Losses: |  |  | $4,051

## Slide 16: Example of a Hazard Mitigation Project
5-year flood = 500’
100-year flood = 504’
10-year flood = 502’
(NEW FFE = 503’)
Hazard doesn’t change, but
its effect on structure does!
After Mitigation (Post-Mitigation)

## Slide 17: Damages to Structure
Post-Mitigation
Flood Depth (feet) | Annual Probability of Flooding | Scenario Damages and Losses | Expected Annual Damages and Losses
0 | 0.20 (5-year flood) | $0 | $0
2 | 0.10 (10-year flood) | $0 | $0
4 | 0.01 (100-year flood) | $6,400 | $64
Total Expected Annual Damages and Losses: |  |  | $64

## Slide 18: Calculation of the BCR
Assume we expect elevated house to last the next 30 years…
Flood Depth (feet) | Expected Annual Damages Before Mitigation | Expected Annual Damages After Mitigation | Expected Annual Avoided Damages and Losses
0 | $1,280 | $ 0 | $1,280
2 | $2,450 | $ 0 | $2,450
4 | $321 | $63 | $258
Totals | $4,051 | $63 | $3,988
PVC (7% Discount Rate, 30 years) |  |  | x 12.41
Net Present Future Value of Future Benefits |  |  | $49,491
Costs |  |  | $35,000
Benefit-Cost Ratio |  |  | 1.41

## Slide 19: General Concept of a BCA
Questions?

## Slide 20: Determining Benefits for a Hazard Mitigation Project

## Slide 21: Determining Benefits For A Hazard Mitigation Project
What types of benefits can you claim for your project?
Avoided Physical Damages
Avoided Emergency Response Costs
Avoided Loss-of-Function Impacts
Avoided Injuries and Casualties
Societal and Environmental Benefits
CLOSED

## Slide 22: Determining Benefits For A Hazard Mitigation Project
Notes: Physical: houses, contents, bridge, pipes, hospital building, hospital equipment
Emergency Response: sandbagging, set up detour, barricades, evacuation LOF: road, utilities, residential, hospital
Injuries and Casualties? (no)
Social: mental stress/anxiety, lost worker productivity, environmental?

## Slide 23: Benefits - Avoided Physical Damages
Damages to facilities requiring repair or replacement:
  Structures
  Contents
Roads
Bridges
Utilities

## Slide 24: Benefits - Avoided Response Cost
Costs include labor, equipment, and materials to perform emergency work, for example:
  Sandbagging before the event
  Costs to evacuate residents
  Costs to close roads
  Costs to provide a temporary by-pass

## Slide 25: Benefits - Avoided Loss-of-Function (LOF)
Loss of function is an interruption to:
  Utilities
  Roads
  Businesses
  Residences
  Critical services
Benefits depend on:
  Value of the function
  Length of interruption

## Slide 26: Benefits - Avoided Loss-of-Function (LOF)
Examples include:
  Mechanical equipment for a hospital damaged in a flood
  Road bridge collapses during an earthquake
  Electric lines down after a wildfire

## Slide 27: Loss-of-Function Data
Roads:
You
  # of one-way traffic trips per day
  # of additional miles and minutes per trip
  Downtime length (days)
FEMA
  Standard value for $/car/hour
Utilities (potable water, wastewater and electrical):
You
  # of customers that will be protected by mitigation project
  Downtime length (days)
FEMA
  Standard value for $/person/day

## Slide 28: Loss-of-Function Data
Ordinary Public Buildings:
You
  Annual operating budget for that building
  Downtime length (days)
FEMA
  No standard values!
Critical Services (police, fire, and medical):
You
  # of people served by facility and type of area (urban vs. rural)
  Distance to closest similar facility
  # served at closest similar facility
  Downtime length (days)
FEMA
  Economic values on a per-day basis

## Slide 29: Loss-of-Function Data
Residential Displacement:
You
  # occupants
  Building type
  Building Replacement Value (BRV)
  Per diem values for your area
FEMA
  Depth-damage curve
Non-residential:
You
  Monthly rental costs for comparable building
  Downtime length (days)
FEMA
  One time disruption cost

## Slide 30: Benefits – Avoided Injuries and Casualties
In CA, only counted for seismic retrofit projects:
You
  average # of occupants in building over a typical 24-hour period
FEMA
  $ value/death or injury

## Slide 31: Injury and Casualty Data
Based on academic research by Department of Homeland Security, the Value of Statistical Life:
Dead - Fatal
$6,900,000
Major Injuries
$1,800,000
Minor Injuries
$14,000
Typically only counted for tornado and earthquake projects due to insufficient warning times

## Slide 32: Societal Benefits
Mental Stress (residential Only)
  $2,443 per person
  BCR must be >0.75 without these benefits for them to kick in
Lost Productivity (residential Only)
  $8,736 per worker
  BCR must be >0.75 without these benefits for them to kick in
Street maintenance
Volunteer time
Loss of rent

## Slide 33: BCAs for Generator Projects
Generators most often funded through the HMGP 5% initiative
For the "regular" HMGP they must have a BCA
No dedicated path in the BCA software
Most often done via DFA methodology

## Slide 34: BCAs for Generator Projects
Power loss frequency is often difficult to determine accurately
Various sources in FEMA guidance; good to have local records if possible
Generally power losses by themselves are not frequent or long enough to generate sufficient benefits to support a project (meaning simply counting the value of lost power) - need to be related to a service like fire department, water/sewer pumps, EOC, etc.

## Slide 35: BCAs for Generator Projects
Loss of service calculations are generally based on the same inputs as other BCAs for public operations and facilities - #served, distance to nearest analogous facility, etc., along with time of interruption
As with all BCAs, documentation is important, especially true of generators, where the burden of proof is on the analyst - not much default data to work with
"Standard Economic Values" guidance has some useful metrics
Work with your local utility provider to determine dates and duration of power loss events
If three or more power loss events, utilize unknown frequency calculator in DFA module to determine recurrence intervals

## Slide 36: Climate Resilient Mitigation Activities (CRMA) Guidance
CRMA projects use nature-based design in their implementation
Green infrastructure or nature based design encourages communities to use more sustainable methods
In September 2015, FEMA released three new activities eligible for the Hazard Mitigation Assistance programs:
  Aquifer Storage and Recovery
  Floodplain and Stream Restoration
  Flood Diversion and Storage

## Slide 37: Climate Resilient Mitigation Activities (CRMA) Benefits
In May 2016, FEMA developed specific tools to evaluate the ecosystem services and how they would fit with the rest of the benefit cost analysis toolkit:
  Drought mitigation
  Ecosystem service
  Pre-calculated benefits for cost effectiveness evaluation of soil stabilization, flood diversion, and reforestation projects in wildfire impacted areas to support expedient implementation of post-wildfire mitigation actions

## Slide 38: Pre-Calculated Benefits
To streamline the HMA grant application process, FEMA has released several benefit-cost efficiencies to provide pre-determined cost effectiveness values
Using pre-calculated benefits eliminates the requirement for applicants to conduct a separate BCA for eligible projects:
  Acquisitions and elevations in the Special Flood Hazard Area (SFHA)
  Residential Hurricane Wind Retrofits
  Non-Residential Hurricane Wind Retrofits
  Individual Tornado Safe Rooms
  Post-Wildfire Mitigation

## Slide 39: Post-Wildfire Mitigation Benefits
FEMA developed pre-calculated benefits to streamline implementation of mitigation actions in wildfire impacted areas to reduce risk from related hazards such as flood
Soil stabilization, flood diversion, and reforestation projects under the cost of $5,250 per acre are determined cost effective and no further BCA is required

## Slide 40: Landslide Pre-Calculated Benefits

## Slide 41: Environmental and Ecosystem Benefits
Environmental and ecosystem service benefits cannot be included with the project until 0.75 is demonstrated by the benefit cost analysis
Essentially what this means is when we have done these projects, you have to have enough benefits to cover 0.75 of the project cost

## Slide 42: Using Sea Level Rise in BCAs
FEMA guidance allows/encourages the use of sea level rise (SLR) in BCAs
Applies to flood analyses
Specific data entry cell for expected SLR in ”full flood” module
Can be used in DFA by incorporating side calculation – adjusting historic or expected frequencies or damages
MUST cite a valid source of sea level rise
FEMA has developed an XL-based calculator that we can provide

## Slide 43: Determining Benefits For Your Hazard Mitigation Project
Questions?

## Slide 44: Components of a BCA

## Slide 45: Components Of A BCA
What kind of information do you need for a BCA?
What natural hazard is your project addressing?
How often does that hazard happen?
How long will your project be effective for?
What damages does this hazard cause to the community?
How much of this damage does your project prevent?

## Slide 46: Components Of A BCA
What natural hazard(s) is your project addressing?
  Floods
  Earthquakes
  Wildfires
  Landslides
  Droughts
  Hurricanes
  Tornados
  Tsunamis

## Slide 47: Components Of A BCA
How often does that hazard occur?
  We can’t predict exactly when it will happen
  But can estimate how often events of various severities occur it based on:
    Historic events
    FEMA flood insurance studies
    FEMA wildland/urban interface fire return periods (included in the fire BCA software by zip code)
    USGS National Seismic Hazard Data (included in the earthquake BCA software)

## Slide 48: Components Of A BCA
How often does that hazard occur?
  Another name for these estimates are recurrence intervals (RI)
    The recurrence interval represents the average period of time between two occurrences of a specific magnitude hazard event
    It is the inverse of the annual probability of an event

## Slide 49: Components Of A BCA
How long will your project be effective for?
  Improvements to the built environment do not last forever
    The retrofit itself may become less effective overtime, even with maintenance
    Or the structure the retrofit is improving becomes too old and needs to be replaced
  This affects how far in the future the BCA evaluates. This time period is known as the project useful life (PUL)
    This affects how much total damage and benefits the BCA will include
  FEMA has standard values for most project types

## Slide 50: Components Of A BCA
What damages does this hazard cause to the community?
  Physical Damages
  Loss of Life
  Loss of Function
  Mental Stress and Anxiety*
  Environmental*
* These benefits can be used only when the underlying BC ratio exceeds 0.75

## Slide 51: Components Of A BCA
How does a BCA calculate damage?
  It calculates how much damage occurs for each level of event
    Ex. $24,500 for a 10-year event, $32,100 for a 100-year event
  It takes the recurrence interval (RI) and calculates the annual probability
    Ex. A 100-year event has a 1/100=0.01 or 1% annual probability of occurring
  It multiples the expected damage and the annual probability to calculate expected annual damages

## Slide 52: Components Of A BCA
How much of this damage does your project prevent?
  Reduce physical damages
  Reduce loss of life
  Reduce loss of function/service
  Reduce mental stress
Most projects do not eliminate all risk
  Have to calculate residual damages that may occur after your project is implemented

## Slide 53: Components Of A BCA
BCA is conceptually:
Compare before-mitigation and after-mitigation damages
If damages are reduced after mitigation, then there are benefits to count
If the benefits are greater than costs, the project is cost-effective
Notes: COME BACK TO THIS SLIDE AFTER EXCEL

## Slide 54: Components Of A BCA
Questions?

## Slide 55: Documenting the BCA

## Slide 56: Documenting The BCA
What things should you include to compile your BCA?
  Damage Frequency Assessment (DFA)
    Most generic module
    Can be used for any hazard type
  Flood
  Wildfire
  Seismic
  Drought (Aquifer Recharge)
  Landslide Acquisition (outside of BCA tool)
  Generators/Early Warning Systems

## Slide 57: Documenting The BCA
For all projects:
  Use data from credible and reliable sources (Federal, state, local agencies)
  Provide complete technical support data – copy of the FIS data (FIRM, discharge data, flood profiles) or reports from other agencies
  Explain and provide justification for data that supersedes FIS or standard FEMA data
  Organize the data via a list of attachments
  Cite the location of BCA relevant data within the support data (i.e., report name, page no., etc.)
  Do not assume that, during review, FEMA has access to the same data that the user does

## Slide 58: Documenting The BCA
For all projects:
  Technical documentation showing level of protection
  Documentation supporting project useful life (PUL) if FEMA standard value not used
  Detailed cost estimate and source of estimate
  Maintenance costs
  Documentation supporting value of service if FEMA standard value is not used
  Documentation of value of building function (annual budget)

## Slide 59: Documenting The BCA
For projects using DFA Module:
  Technical documentation supporting recurrence intervals
    Precipitation data, stream gage data
    Fault rupture data
    Utility outage data (weather related)
  Analysis of expected damages for each level of hazard
    Pre-mitigation AND post-mitigation
  Documentation of historic damages with dates

## Slide 60: Documenting The BCA
For projects using Flood Module:
  Documentation of first floor elevation
    Elevation certificate
    LIDAR + offset based on foundation
  Documentation of flood hazard
    H&H Analysis (flood elevations, discharge rates, RIs)
      Flood Insurance Study (FIS) is an H&H analysis!
  Justification for any revisions to the FEMA depth-damage curves – its almost always best to use the FEMA values

## Slide 61: Documenting The BCA
For projects done in Wildfire Module:
  Defined project area (see notes on your fire summary)
  Justification for mean fire return period if FEMA data per zip code is revised
  Documented population of project area
  Documented number of structures in project area
  Documented building replacement values in project area
    Professional construction estimate
    Reputable construction estimation data (RS Means, etc.)

## Slide 62: Documenting The BCA
For projects done in Seismic Module:
  Justification of soil type
    Geotechnical report or USGS soil/rock data (VS 30, etc.)
    Soil type D may be used if soil/rock type is unknown
  Documentation of building replacement value
  Documentation of the average occupancy on a 24/7/365 basis
    Averaged over a typical year
    Show activities or programs with duration and # of participants
  Justification for pre- and post- mitigation design levels
  Analysis for any non-default seismic building parameters

## Slide 63: Documenting The BCA
For projects done in Drought (ASR) Module:
  # of people served by aquifer
  Total demand of aquifer (mgd)
  Drought RIs
  Analysis of pre-mitigation reduced supply
  Analysis of post-mitigation reduced supply

## Slide 64: Documenting The BCA
Quick discussion of 2015 Climate-Resilient Mitigation Activities (CRMA)
Guidance at:
  http://www.fema.gov/climate-resilient-mitigation-activities-hazard-mitigation-assistance

## Slide 65: Using The FEMA BCA Tool

## Slide 66: Using The FEMA BCA Tool
Walkthrough of example projects

## Slide 67: DFA EXAMPLE

## Slide 68: DFA EXAMPLE

## Slide 69: DFA EXAMPLE

## Slide 70: DFA EXAMPLE

## Slide 71: DFA EXAMPLE

## Slide 72: DFA EXAMPLE

## Slide 73: DFA EXAMPLE

## Slide 74: DFA EXAMPLE

## Slide 75: DFA EXAMPLE

## Slide 76: DFA EXAMPLE

## Slide 77: DFA EXAMPLE

## Slide 78: DFA EXAMPLE

## Slide 79: DFA EXAMPLE

## Slide 80: DFA EXAMPLE

## Slide 81: DFA EXAMPLE

## Slide 82: DFA EXAMPLE

## Slide 83: DFA EXAMPLE

## Slide 84: DFA EXAMPLE

## Slide 85: DFA EXAMPLE

## Slide 86: DFA EXAMPLE

## Slide 87: DFA EXAMPLE

## Slide 88: QUESTIONS?
Questions?

## Slide 89: WILDFIRE EXAMPLE

## Slide 90: WILDFIRE EXAMPLE

## Slide 91: WILDFIRE EXAMPLE

## Slide 92: WILDFIRE EXAMPLE

## Slide 93: WILDFIRE EXAMPLE

## Slide 94: WILDFIRE EXAMPLE

## Slide 95: WILDFIRE EXAMPLE

## Slide 96: QUESTIONS?
Questions?

## Slide 97: EQ Module

## Slide 98: EQ Module

## Slide 99: EQ Module

## Slide 100: EQ Module: Building retrofit

## Slide 101: EQ Module: Mitigation Type

## Slide 102: EQ Module: Cost Estimator

## Slide 103: EQ Module: Cost Estimator

## Slide 104: EQ Module: Soil and Element Information

## Slide 105: EQ Module: Building Information

## Slide 106: EQ Module: Building Information

## Slide 107: EQ Module: Vulnerability

## Slide 108: EQ Module: Vulnerability

## Slide 109: EQ Module: Loss of Service

## Slide 110: EQ Module: Loss of Service

## Slide 111: EQ Module: Volunteer Costs

## Slide 112: EQ Module: Analysis (before  after)

## Slide 113: EQ Module: BCR Results

## Slide 114: EQ Module: Anchorage

## Slide 115: EQ Module: Anchorage

## Slide 116: EQ Module: Anchorage

## Slide 117: EQ Module: Mitigation Type

## Slide 118: EQ Module: Cost Estimator

## Slide 119: EQ Module: Soil and Element Information

## Slide 120: EQ Module: Hazard Data

## Slide 121: EQ Module: Damage State Information

## Slide 122: EQ Module: Functional Downtime

## Slide 123: EQ Module: Element Value-Fall Area

## Slide 124: EQ Module: Occupancy and Casualty Data

## Slide 125: EQ Module: Secondary Damages

## Slide 126: EQ Module: Loss of Service
Volunteer Costs

## Slide 127: EQ Module: Summary of Damages

## Slide 128: EQ Module: BCR Results

## Slide 129: EQ Module: Project Summary

## Slide 130: Questions?
Questions?